## Slide 1: Algorithms for Complete Physiological Monitoring During Spaceflight
Aven Zitzelberger, Undergraduate, Computer Science and Engineering
Dr. Mohammad Ghassemi, Assistant Professor, Computer Science
A great deal of research is being done on the topic of health monitoring, especially when it comes to methods that are invasive or time consuming. Much of this research focuses of on the extrapolation of bio-signals from different measurements. For example, PPG readings can be used to reconstruct ECG data1. Similarly, ECG and PPT data can be used to predict blood pressure readings2. Consequently, it is possible to extrapolate blood pressure from PPG and PPT data, and it has been done with up to 95% accuracy using machine learning models3. Clearly, This technology is extremely beneficial in monitoring bio-signals and diagnosing health risks, especially in the context of spaceflight4.
Motivation
In the environment of a spacecraft, continuous passive monitoring of astronaut physiology is of critical importance. Current approaches to comprehensive health monitoring require a cumbersome array of various sensors which limit the mobility and comfort of astronauts and are collectively prone to malfunction. Together, these factors motivate the development of physiological monitoring algorithms that can accurately reconstruct a missing sensor’s data, using the values of the other measurements available.
Previous Research
Objectives
Next Steps
References
Fig. 2: Wireless EEG setup.
Methods
[1] Q. Zhu, X. Tian, C.-W. Wong, and M. Wu, “ECG Reconstruction via PPG: A Pilot Study,” in 2019 IEEE EMBS International Conference on Biomedical Health Informatics (BHI), May 2019, pp. 1–4, doi: 10.1109/BHI.2019.8834612.
[2] O. Viunytskyi, V. Shulgin, V. Sharonov, and A. Totsky, “Non-invasive Cuff-less Measurement of Blood Pressure Based on Machine Learning,” in 2020 IEEE 15th International Conference on Advanced Trends in Radioelectronics, Telecommunications and Computer Engineering TCSET), Feb. 2020, pp. 203–206, doi: 10.1109/TCSET49122.2020.235423
[3] D. Jia and W. Yin, “Continuous blood pressure prediction based on hierarchical adaptive algorithm,” in 2020 IEEE 4th Information Technology, Networking, Electronic and Automation Control Conference (ITNEC), Jun. 2020, vol. 1, pp. 934–938, doi: 10.1109/ITNEC48623.2020.9084725.
[4] J. M. Eklund and N. Khan, “A bio-signal computing platform for real-time online health analytics for manned space missions,” in 2018 IEEE Aerospace Conference, Mar. 2018, pp. 1–8, doi: 10.1109/AERO.2018.8396819.
Fig. 3: Three EEG channels (F7, F8, and F4) viewed through a browser window. The decreases in voltages correspond to the subject’s eyes being closed.
Fig. 1: Raspberry Pi sensor hub. From left to right: Sense Hat, Picam, and the OpenBCI dongle.
Given the importance of physiological monitoring, the idiosyncratic nature of physiological waveforms, and the practical constraints of moving equipment into orbit, our objectives are to (1) develop algorithms that enable reliable, real-time reconstruction of missing physiological waveforms using one or more other available waveforms and to (2) discover the minimal subset of monitoring systems needed to obtain the best overall picture of physiological status.
Continuing this project, we will use publicly available bio-signal datasets to train a deep encoder-decoder network that can reconstruct the values of a missing waveform, using all other available waveforms. We expect to see robust correlations between physiological waveforms that will allow us to identify potentially redundant health monitoring hardware for a spaceflight environment.
After this initial demonstration of efficacy, we will collect physiological and behavioral data of subjects performing multiple tasks in a laboratory environment. Following model development, we will test the ability of models trained on earth to be effectively tuned to new subjects and new tasks using transfer learning. This last point is of particularly importance as it will enable our methods to be tuned to individual astronauts after they’ve arrived on a spacecraft.
Ultimately, we will endeavor to build a system that is able to accommodate for signal loss, unavailability, or device malfunction via reconstruction of any missing information. This software would be used aboard a spacecraft to continually monitor astronaut health while they remain mobile and enable real-time prediction of health issues or concerns before they could normally be detected.
Data is collected from three sources, also shown in the figures to the right. The Pi Sense Hat streams temperature, humidity, pressure, and gyroscopic data, the Picam streams a live video feed, and the OpenBCI EEG headset stream EEG data to its corresponding dongle on the Raspberry Pi. These data streams are organized and packaged by the Pi, then streamed to our data-ingestion server for analysis. The data can then be viewed in a browser window after processing.
Acknowledgements:
This work was supported by the Michigan Space Grant Consortium (Grant No. NNX15AJ20H).
Blinks
Eyes closed
Notes: Algorithms for complete physiological monitoring during space flight.
This project was created by Aven Zitzelberger and Dr. Mohammad Ghassemi of Michigan State University, and funded in part by the Michigan Space Grant Consortium.
–––––––––––
The motivation for this research begins with the critical importance of continuous and non-invasive monitoring of the health of astronauts while aboard a spacecraft like a Shuttle or the ISS.
Current methods of monitoring health require many sensors that are often limiting in mobility and uncomfortable, and some devices such as a blood pressure cuff, are simple not meant to be continually worn.
Additionally, replacement devices are not readily available while in orbit in the event that any should break or malfunction.
Together these factors motivate the development of an algorithm that can accurately reconstruct a missing sensor’s data, using the values obtained from the remaining measurements.
–––––––––––
Much research is being done in the field of medical monitoring, especially when it comes to reducing the limitations of non-invasive methods. Some of this research focuses in particular on the extrapolation of bio-signals from various other measurements, for example, data from a photoplethysmogram can be used to reconstruct some Ecocardiogram readings, including Pull Transit Time, which in turn can be used to reconstruct blood pressure measurements. This is particularly beneficial as blood pressure is a very difficult measurement to take, as inflatable cuffs are time consuming, and intravenous sensors are far too invasive to be used for long periods of time.
––––––––––-
Our objective are twofold: First we will develop algorithms that enable reliable, real-time reconstruction of data from missing sensors using the information from those available. Second, we will endeavor to discover the minimal subset of monitoring sensors necessary to obtain the most accurate overall picture of physiological status while maintaining comfort.
––––––––––
To demonstrate the efficacy of these objectives, we will first be building software to stream real-time health sensor data to a remote server for analysis. Our current methods consist of collecting data from three sources, as shown in these figures. The Raspberry Pi Sense hat, seem on the left of figure 1, collects temperature, humidity, pressure, and gyroscopic data. The Picam in the middle, streams a live video feed. The USB dongle on the right receives data from our Wireless OpenBCI board, which streams EEG, EMC, and ECG readings of a subject, seen in figure 2. The data from these sources is collected and packaged by the respbeerry pi and streamed to our remote server for analysis. Once processed, our software hosts a service through which the data can be viewed in real-time through any browser window, as demonstrated in figure 3, containing three channels of EEG data, The demonstrated drops in voltage correspond to the subject blinking and closing their eyes.
––––––––––
To continue this project, we will begin by using a publicly available bio-signal dataset to train a deep encoder-decoder neural network that can reconstruct the values of a missing waveform. We expect to see robust correlations between various physiological waveforms that will allow us to identify potentially redundant monitoring hardware. Following this, we will collect physiological and behavioral data from subjects performing multiple tasks in a laboratory environment, where we will test the ability of our models to accurately preduct sensor measurements. We will then test our models on their effectiveness in functioning with new subjects and new tasks. Ultimately, we will endeavor to build a system that is able to accommodate for signal loss, or device malfunction via reconstruction of the missing information. The software would be invaluable aboard a spacecraft to continually monitor astonaut health while they remain mobile and enable real-time prediction of health issues or concerns before the could normally be detected.